If you do not feel comfortable doing this procedure please take your car to a shop that has experience doing this.
This is straight from the factory manual.

Bleeding the spoiler pump unit

Reduced 41% 592 x 676 (207.01K)

1. Pulling out pump
Pull hydraulic cylinder 2 out to the dimension Y = 35 +2 mm . To do this, connect 12 V to the pump. Observe polarisation arrangement A.
2. Bleeding short hydraulic line
Slowly tighten short hydraulic line 4 until the hydraulic cylinder 2 moves. If the hydraulic cylinder has reached the lower mechanical stop inset X, push back onto the stop if necessary, hydraulic lines must be laid parallel to each other inset Z. Tighten banjo bolt 3. Tightening torque: 15 Nm (11 ftlb.)
3. Bleeding long hydraulic line
Slowly tighten long hydraulic line 5 until the hydraulic cylinder 2 moves. If the hydraulic cylinder has reached the lower mechanical stop inset X, push back onto the stop if necessary, hydraulic lines inset Z must be laid parallel to each other. Tighten banjo bolt 3. Tightening torque: 15 Nm (11 ftlb.)

Note: Use only Pentosin CHF 11 S (or it's replacement). 

This post has been edited by Loren: Oct 29 2007, 05:03 PM

Reason for edit: Added fluid type

--------------------

Loren
RennTech.org
PCA member since 1978
My Mods in the Registry · My Blog